## Slide 1: CubeSat Electrical Power System (EPS)
Objective:
To design and implement a miniature satellite power management system that simulates energy generation, storage, and distribution.
Team Members: [Add Names]
Supervisor: [Add Name]

## Slide 2: Project Overview
CubeSats require a reliable Electrical Power System (EPS) to:
- Generate power (via solar panels)
- Store energy (in batteries)
- Distribute power (through converters and controllers)
Our mock-up replicates this using solar panel imitation, STM32 controller, and telemetry for monitoring.

## Slide 3: System Components
1. Solar Panels / Simulators
2. Battery (Li-ion / Li-Po) with BMS
3. DC-DC Converters for 5V and 3.3V
4. STM32 Microcontroller for control and monitoring
5. Load Simulation using LEDs, fans, or small modules

## Slide 4: System Architecture
Power Flow:
Solar Panel → Charge Controller → Battery → DC-DC Converters → Loads
Control Flow:
STM32 monitors current, voltage, state of charge, and temperature, controlling load switching & safety.

## Slide 5: Circuit Design
Main Sections:
- Charging Stage: Solar panel + TP4056 charge controller ( for battery charging )
- Storage Stage: Battery + BMS
- Conversion Stage: DC-DC converters
- Measurement: Voltage dividers + INA219 or ACS712 current sensors

## Slide 6: STM32 Controller Functions
- Read battery voltage and current through ADC
- Estimate State of Charge (SOC)
- Manage charging/discharging
- Cut off power when voltage is too low
- Communicate telemetry data via UART/Bluetooth

## Slide 7: Telemetry and Data Visualization
Purpose: To monitor satellite power health in real time.
Features:
- Display battery voltage, current, and temperature
- Live graphing of charge/discharge cycles
- Data transmission via UART or Bluetooth

## Slide 8: Load Simulation
LEDs, fans, or motors simulate subsystems.
Controlled by MOSFETs via STM32.
Goal: Demonstrate realistic power distribution.

## Slide 9: Software & Firmware Design
Firmware (STM32):
- ADC readings
- Power mode logic
- UART/Bluetooth communication
PC Interface:
- Serial visualization
- Graphs and system alerts

## Slide 10: Expected Results
- Stable 5V and 3.3V outputs
- Accurate telemetry reporting
- Automatic charge/discharge control
- Realistic simulation of CubeSat EPS

## Slide 11: Future Improvements
- Integrate MPPT
- Add temperature compensation
- Implement LoRa telemetry
- Fabricate a PCB prototype

## Slide 12: Conclusion
The CubeSat EPS mock-up demonstrates:
- Efficient power management
- Safe battery operation
- Real-time telemetry & visualization
Outcome: Functional miniature model of real CubeSat EPS.

## Slide 13: References
- CubeSat Design Specification (Cal Poly SLO)
- STM32 Datasheet & HAL Documentation
- TP4056 & INA219 Datasheets
- Research papers on CubeSat EPS design

## Slide 14: Q&A
Thank you!
Questions?